## Slide 1
🔥
Thermal Hotspot
Prediction in
Electronic Chips
Using Machine Learning
Saumya Singhal | 230940
ME644 • IIT Kanpur

## Slide 2
Why Chips Overheat
The thermal challenge in modern electronics
⚡
Billions of transistors
Each switching event dissipates heat. Modern CPUs generate heat densities of 10–100 W/mm².
🌡️
Uneven heat distribution
CPU cores run 10–15× hotter than memory blocks, creating localised 'thermal hotspots'.
🐌
Thermal throttling
Chip automatically slows down to prevent damage — visible as sudden performance drops.
⏳
Electromigration & aging
High temperatures push metal atoms apart, causing microscopic breaks and shortened lifespan.
Traditional Simulation
✓ Highly accurate ✗ Hours per simulation ✗ Cannot explore 1000s of designs ✗ Not feasible in design flow
ML Surrogate Model
✓ Millisecond inference ✓ 1000s of designs explored ✓ Trained once, used forever

## Slide 3
Physics of Heat Flow
Fourier's law, thermal resistance stack & the Gaussian hotspot model
Governing Equation (Fourier's Law)
∇ · [k(x)∇T(x)] + Q(x) = 0
k = conductivity Q = heat generated T = temperature
Ohm's Law Analogy
ΔT = Q × Rθ,total
Like V = IR — more resistance → more temperature rise
Gaussian Hotspot Temperature Model
T(x,y) = T_boundary + Q_base × R_total + Q_block × exp[-(x-x₀)² + (y-y₀)²) / 2σ²] × R_local
Heat Sink
TIM Layer
Heat Spreader (IHS)
Metal Interconnects (Cu/W)
Silicon Die (Active Layer)
Package Substrate
PCB / Motherboard
Thermal Stack (Cross-Section)
HIGH T
LOW T

## Slide 4
Dataset Generation
12,000 physics-informed synthetic samples with 14 input features
Why Synthetic?
Real chip thermal data is highly confidential (Intel, AMD, NVIDIA treat it as IP). We use the known physics equation to generate unlimited, realistic, labelled samples — called a physics-informed dataset.
Heat Source
▸ power_density (1–8 W/mm²)
▸ block_power_map (0.5–15 W/mm²)
Silicon Die
▸ thermal_cond_si (100–170 W/m·K)
▸ die_thickness (0.3–0.8 mm)
Packaging
▸ tim_hs_conductance (0.3–1.2 W/cm²K)
▸ boundary_temp (290–330 K)
▸ metal_cond_Cu
▸ metal_cond_W
Spatial / Hotspot
▸ x, y (query coordinates)
▸ hotspot_cx, hotspot_cy
▸ sigma_spot (spread radius)
▸ r_sq = (x-x₀)² + (y-y₀)²
💡 Key Insight
r_sq is derived from x, y, hotspot_cx, hotspot_cy — but pre-computing it gives linear models a chance to approximate the Gaussian decay.
12,000
Total Samples
9,600 / 2,400
Train / Test Split

## Slide 5
Data Preprocessing & Feature Insights
Correlation analysis, scaling, and quality checks
Pearson Correlation with Temperature
boundary_temp
+0.697
power_density
+0.516
die_thickness
+0.349
thermal_cond_si
-0.194
r_sq
-0.122
block_power_map
+0.063
Feature Scaling (Z-score)
x̃ⱼ = (xⱼ − μⱼ) / σⱼ
• Applied to OLS and MLP (not RF)
• Scaler fitted on training set only — prevents data leakage
• Ensures equal gradient weight across all features
⚠️ Why is block_power_map correlation so low?
Despite being physically crucial (drives the hotspot), block_power_map has r = 0.063 with temperature.
Reason: Its effect depends entirely on proximity (r_sq). At hotspot centre: huge effect. Far away: negligible effect. This spatial interaction is inherently nonlinear — linear correlation misses it entirely.
This is exactly why nonlinear models outperform linear ones.

## Slide 6
Machine Learning Models
📐 Linear Regression
Linear Baseline
Weighted sum of 14 features + regularisation. Interpretable coefficients. Cannot model the Gaussian exponential.
🌲 Random Forest
Nonlinear Ensemble
200 decision trees, each seeing a random data subset. Piecewise-constant approximation of the nonlinear physics.
🧠 Neural Network (MLP)
Smooth Nonlinear
Architecture: 14→128→64→32→1, ReLU activations, Adam optimiser. Smooth differentiable function approximator.

## Slide 7
Model Performance — Quantitative Results
Test set (n = 2,400) across all metrics
Model | R² ↑ | RMSE (K) ↓ | MAE (K) ↓ | Max Error (K) ↓ | CV R²
OLS Linear Reg. | 0.9186 | 4.720 | 3.413 | 40.53 | 0.920 ± 0.004
Random Forest | 0.9524 | 3.610 | 2.315 | 31.95 | 0.950 ± 0.002
Neural Net (MLP) ★ | 0.9797 | 2.355 | 1.831 | 10.45 | 0.982 ± 0.002
🎯 MLP wins all metrics
Best R², RMSE, MAE and Max Error — comprehensive superiority
⚠️ Max Error matters most
OLS worst-case: 40.53 K. MLP: 10.45 K. 4× safety improvement.
✓ No overfitting
CV R² tracks test R² closely for all models.

## Slide 8
Performance Comparison Charts
R², RMSE, and MAE across all models
Clear trend: OLS → RF → MLP | Each step adds nonlinear expressiveness and reduces error

## Slide 9
Why Max Error Matters — The Hotspot Challenge
The Gaussian nonlinearity is where models fail or succeed
Worst-Case Prediction Error
OLS
40.53 K
Random Forest
31.95 K
MLP
10.45 K
4× improvement in worst-case error
The Gaussian Nonlinearity Challenge
ΔT_hotspot = Q_block × exp(−r²/2σ²) × R_local
This 3-way interaction (Q_block, r², σ) inside an exponential is fundamentally nonlinear. Errors are worst at hotspot centres where this term peaks.
OLS:
Can only fit w·r² — misses the exponential entirely. Predicts too LOW at hotspot centre.
Random Forest:
Piecewise-constant approximation. Blocky prediction near the sharp peak.
MLP:
Smooth function composition across layers. Approximates the exponential decay almost perfectly.

## Slide 10
Spatial Thermal Map & 3D Surface
Gaussian hotspot shape predicted by the models — hotspot at (5,5) mm, σ=0.08
RF Predicted Thermal Map
Hotspot at (5,5) mm, σ=0.08
Temperature Cross-Section Insights
OLS: Severely underestimates hotspot peak. Cannot follow exponential — systematic error pattern. Too low at centre, too high at mid-distance. Random Forest: Captures peak shape but in a 'blocky', stepped manner. Piecewise-constant nature can't follow smooth curves. MLP: Follows the true physics curve almost perfectly, including the sharp central peak.
Chart: Temperature Cross-Section Through Hotspot Centre
| 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
True Physics | 328 | 328.5 | 329.5 | 332 | 337 | 348 | 337 | 332 | 329.5 | 328.5 | 328
MLP | 328.1 | 328.6 | 329.7 | 332.2 | 336.8 | 347.5 | 336.8 | 332.2 | 329.7 | 328.6 | 328.1
Random Forest | 328 | 328 | 329 | 331 | 336 | 345 | 336 | 331 | 329 | 328 | 328
OLS/Ridge | 329 | 329.5 | 330.5 | 332.5 | 334.5 | 336 | 334.5 | 332.5 | 330.5 | 329.5 | 329

## Slide 11
Discussion: Why Each Model Performs As It Does
Physical reasoning behind the performance gap
📐 Linear Models — Hard Ceiling at R² = 0.92
The governing equation contains exp(−r²/2σ²) — a 3-way nonlinear interaction
Linear models can only fit: w₁·r² + w₂·σ + w₃·Q_block (additive)
Cannot represent the product-inside-exponential structure
No amount of data or tuning can overcome this structural limitation
The 0.08 gap in R² directly quantifies the 'locked-in' nonlinear physics
🌲 Random Forest — Piecewise Approximation at R² = 0.95
Approximates Gaussian via recursive binary splits on r², σ, Q_block
E.g. 'if r² < 0.01 AND σ < 0.1 AND Q > 10 → predict 370 K'
200 trees average away individual variance — strong ensemble effect
OOB R² = 0.9524 matches test R² exactly — robust validation
Remaining gap: piecewise-constant predictions can't follow smooth curves
🧠 Neural Network — Near-Perfect at R² = 0.98
Universal approximation theorem: MLP can approximate any smooth function
Smooth, differentiable predictions — can follow the exponential curve exactly
Layer 1 learns linear combinations; Layer 2–3 compose nonlinear interactions
Early stopping prevents overfitting — generalises to unseen test data
Result: smooth, physically-accurate thermal surface prediction

## Slide 12
Limitations & Scope
✅ What This Model DOES
Predicts temperature at any spatial point given chip properties and known hotspot location
Works for steady-state (equilibrium) thermal conditions
Models a single Gaussian hotspot per sample
Provides fast surrogate predictions (milliseconds vs hours for FEM)
Delivers physically consistent, interpretable results
❌ What This Model Does NOT Do
Does NOT discover where hotspots are — hotspot location is a required input
Does NOT handle multiple overlapping heat sources (real chips have many)
Does NOT model transient (time-varying) workloads or thermal dynamics
Does NOT use real chip measurements — synthetic data needs real-world validation
Does NOT generalise to chip architectures outside the training parameter ranges

## Slide 13
Conclusions & Future Work
1
MLP is the best model
R² = 0.9797, RMSE = 2.355 K, Max Error = 10.45 K — near-perfect thermal prediction
2
Nonlinear gap quantified
Linear models ceiling at R² = 0.919 due to the Gaussian physics. The 0.06 gap is structurally locked.
3
3
Physical consistency
All models learn correct sign and magnitude relationships — physically trustworthy
4
Top 5 features = 96.8%
boundary_temp, power_density, die_thickness, thermal_cond_si, r_sq dominate chip temperature
Future Work:
▸ Physics-Informed NNs (PINNs)
▸ CNN for full thermal map
▸ Graph NNs for multi-hotspot
▸ Transient LSTM modelling
▸ Real chip validation